## Slide 1
Modern Control Methods
for Agricultural Irrigation
MPC vs. Reinforcement Learning in Water-Constrained Crop Systems
Tara Torbati | ITMO University, R4237c
Supervisor: Peregudin A. A. | MSc Defence, 2026
Study site: Gilan Province, Iran • 6 ha Hashemi rice field • 38.298°N, 48.847°E

## Slide 2
Presentation Outline
01
Motivation & Problem Statement
02
Simulation Environment (ABM)
03
Controller Designs — MPC & SAC
04
Experimental Setup
05
Results: Baselines & MPC
06
Results: SAC Training & Evaluation
07
Head-to-Head Comparison
08
Conclusions & Future Work

## Slide 3
Motivation: The Anthropogenic Drought Crisis
70%
of global freshwater
consumed by agriculture
40%
of world population
under water stress by 2030
238k
hectares of paddy
in Gilan Province alone
The Control Engineering Gap
Traditional irrigation is reactive and open-loop; no forecast, no constraint awareness
MPC can enforce strict seasonal water budgets but requires expensive online optimisation
RL offers millisecond-latency decisions after training but constraint satisfaction is not guaranteed
This thesis rigorously benchmarks both on a high-fidelity ABM of a real Iranian rice field

## Slide 4
The Simulation Environment: Agent-Based Model
130 crop-soil agents on 10×13 DEM grid
Elevation range 74–181 m (Talish Mountains)
25-year NASA POWER climate dataset (2000–2025)
Cascade water routing  eliminates 'bathtub' mass-balance errors
Decoupled surface & subsurface hydrology (corrects original framework)
Drought stress integrated into biomass eq. (FAO AquaCrop approach)
Per-agent state vector
x₁ Root moisture (mm)
x₂ Thermal time (GDD)
x₃ Maturation stress
x₄ Biomass (g/m²)
x₅ Surface ponding (mm)

## Slide 5
Crop & Scenario Parameterisation
Hashemi Rice
Cultivar
Hashemi rice
Season
DOY 141–233 (93 days)
Kc
1.15 | Depletion p = 0.20
Root depth
400 mm | HI = 0.45
Drought sens. θ₁₄
0.80 (high)
Maturity GDD
1 250 °C·day
Test Scenarios
39.7 mm
Dry 2022
108.8 mm
Moderate 2018
176.8 mm
Wet 2024

## Slide 6
MPC Design: Cost Function & Calibration
Five-term cost function J (recommended operating point α*)
α₁ = 1.0
Terminal biomass reward
anchor term
α₂ = 0.016
Water cost (Iranian domestic-base tariff)
7 000 toman/m³
α₃ = 0.1
Drought stress regulariser
<1% yield sensitivity
α₅ = 0.005
Actuator smoothing ΔU²
tie-breaking
α₆ = 8.0
FC-overshoot soft penalty (x₁ > FC)
eliminates waterlogging
Hp* = 8 days | 3 120 decision vars, 2 081 constraints (per step) | warm-start: 2.5× solver speedup | solver: CasADi + IPOPT

## Slide 7
SAC Design: CTDE Architecture
Actor (deployed online)
Input: 62-dim per-agent obs
(5 local + 57 global features)
Arch: 62 → 128 → 128 → 1
Shared weights across all 130 agents
Output: 130 actions in ~1 ms (CPU)
Critic (training only)
Input: 837-dim (707 obs + 130 actions)
Arch: 837 → 256 → 256 → 1
Never used at deployment time
CTDE
707-dimensional observation space
650-dim
Per-agent block
5 states × 130 agents
9-dim
Global scalars
(day, budget, weather)
48-dim
8-day forecast
(6 vars × 8 days)

## Slide 8
Experimental Setup: 9-Cell Evaluation Grid
Scenario \ Budget
100% 484 mm
85% 411 mm
70% 339 mm
Dry (2022)
1×MPC + 5×SAC
+ 1 fixed-schedule
1×MPC + 5×SAC
+ 1 fixed-schedule
1×MPC + 5×SAC
+ 1 fixed-schedule
Moderate (2018)
1×MPC + 5×SAC
+ 1 fixed-schedule
1×MPC + 5×SAC
+ 1 fixed-schedule
1×MPC + 5×SAC
+ 1 fixed-schedule
Wet (2024)
1×MPC + 5×SAC
+ 1 fixed-schedule
1×MPC + 5×SAC
+ 1 fixed-schedule
1×MPC + 5×SAC
+ 1 fixed-schedule
Data split: 20 training | 3 dev | 3 test years (stratified by rainfall tercile)
Test years never touched during training or hyperparameter selection.

## Slide 9
Baseline Results: No-Irrigation & Fixed Schedule
Chart: Yield (kg/ha) by Scenario
| Dry | Moderate | Wet
No Irrigation | 1462 | 1478 | 2243
Fixed 100% | 3607 | 3302 | 2790
Fixed 85% | 3394 | 3089 | 2901
Fixed 70% | 3118 | 2841 | 3024
Key Findings
Wet 100% fixed: 83.7 waterlog-days
Reducing budget to 70% in wet year INCREASES yield (2790 → 3024 kg/ha)
Fixed schedule cannot respond to dry spells
Open-loop scheduling is fundamentally inadequate
⚠ Wet year: fixed-schedule 83.7 waterlog-days vs. MPC 19.0 days

## Slide 10
MPC Results: Perfect Forecast, Hp = 8
Cell | Yield (kg/ha) | Water (mm) | Wlog-d | Wall-min
Dry / 100% | 4 145 | 469.1 | 0.8 | 44.1
Dry / 85% | 4 069 | 409.9 | 0.3 | 32.7
Dry / 70% | 3 766 | 338.7 | 1.4 | 22.0
Moderate / 100% | 3718 | 399.8 | 5.8 | 85.2
Moderate / 85% | 3 725 | 397.4 | 5.5 | 375.6
Moderate / 70% | 3 612 | 338.6 | 1.3 | 31.9
Wet / 100% | 3 759 | 310.2 | 19.0 | 43.1
Wet / 85% | 3 743 | 308.3 | 16.9 | 48.3
Wet / 70% | 3 754 | 307.8 | 18.2 | 51.0
+14.9%
vs fixed-schedule
dry/100%
+34.7%
vs fixed-schedule
wet/100%
64%
budget used
wet year

## Slide 11
SAC Training: Three-Phase Trajectory
0 – 25k steps
Phase 1
Healthy Convergence
Critic loss 2713 → 0.67
Full-season completion ✓
25k – 96k steps
Phase 2
Productive Plateau
Best eval R = −0.37
best_model.zip captured ✓
96k – 200k steps
Phase 3
Q-value Divergence
Critic loss → 84 693
ent_coef spike 0.03 → 1.29
Root Causes of Divergence
c_term = 5: terminal bonus 300× larger than per-step rewards → Bellman error accumulation
130-dim joint action: critic Q(s,a) overfits; double-Q overestimation accumulates
target_entropy = −13: near-deterministic policy starves critic of action-space coverage
No gradient clipping: large critic updates → larger errors → positive feedback loop

## Slide 12
SAC Evaluation: Seed 0, Best Model (~step 96k)
Chart: Yield at 100% Budget (kg/ha)
| Dry | Moderate | Wet
No Irrigation | 1462 | 1478 | 2243
Fixed Schedule | 3607 | 3302 | 2790
MPC Hp=8 | 4145 | 0 | 3759
SAC | 2477 | 2376 | 3145
SAC Findings
39–70% budget utilised (never hits constraint)
~2–3 mm/day constant schedule — not scenario-adaptive
Applies MORE water in wetter years (opposite of optimal)
Inference: ~1 ms (25 000× faster than MPC)
Wet-year outperformance over fixed-schedule is coincidental, not learned behaviour.
Training pathology — not an inherent RL limitation. Known fixes specified for next run.

## Slide 13
Head-to-Head: The Core Comparison
Chart: Yield Delta vs. Fixed Schedule (kg/ha) [positive = better]
| Dry/100% | Dry/85% | Dry/70% | Wet/100% | Wet/85% | Wet/70%
MPC vs Fixed | 538 | 675 | 648 | 969 | 842 | 730
SAC vs Fixed | -1130 | -910 | -617 | 355 | 247 | 131
MPC Hp=8: +492 to +969 kg/ha over fixed schedule in all completed cells
SAC seed 0: −617 to −1130 kg/ha (dry/mod) | +131 to +355 kg/ha (wet, coincidental)

## Slide 14
Computational Cost: The Deployment Argument
25.9 min
wall-clock per day
MPC mean per-decision
~1 ms
CPU inference
SAC mean per-decision
25 000× faster
SAC:
0.3 s total season | cold start 41 ms | compatible with edge MCU at 3 ms budget
MPC:
22–51 wall-min per season | worst-case single call: 274 s | requires high-performance CPU

## Slide 15
Recommended Fixes for Next SAC Training Run
P1
Remove terminal bonus
Set c_term = 0. Per-step reward integrates to equivalent total biomass signal, distributed smoothly. Eliminates the 300× reward-concentration that causes Bellman error amplification.
P2
Add gradient clipping
max_grad_norm = 1.0 in SAC constructor. Breaks the positive feedback loop: large critic loss → large gradients → larger errors.
P3
Learning rate decay
Linear 3×10⁻⁴ → 5×10⁻⁵ over 500k steps. Prevents noisy late-training updates from destabilising a near-converged Q-function.
P4
Relax target entropy
−13 → −20 to −25 (−0.15 to −0.2 × dim). Improves action-space coverage in late training, reducing Q-overestimation at distribution edges.

## Slide 16
Conclusions
✓
MPC outperforms fixed-schedule by 492–969 kg/ha across all completed cells; waterlogging virtually eliminated.
◎
SAC currently underperforms MPC significantly due to a training pathology (Q-value divergence)
⏳
Forecast-noise evaluation runs are to be completed
⚡
SAC delivers 25 000× faster inference (1 ms vs 25.9 min per day), enabling real-time edge deployment. The computational argument for RL holds even before agronomic parity is reached.

## Slide 17
Thank You
Questions & Discussion
Tara Torbati | ITMO University R4237c | Supervisor: Peregudin A. A.
github.com/taratorbati/thesis