## Slide 1
Study of Modern Control Methods for Agricultural Irrigation Systems
Student: Tara Torbati, gr. R4237c
Supervisor: Alexey A. Peregudin
Saint Petersburg 2026
ITMO University

## Slide 2
2
Motivation
Notes: motivation (here i need to talk about both my country's current water crisis + modern methods of agriculture and precision agriculture + overview of already existing materials and get to the research gap at the end)

## Slide 3
Research Goal
The aim was to study the applications of Modern Control Methods in Agricultural Irrigation of a field in Talish mountains, Gilan province Iran under water scarcity
Field and data selection and preprocessing
Mathematical Modeling of the agricultural system
Controller Design and Simulation (MPC vs RL)
Performance Analysis and Comparison of Results
3
Notes: motivation (here i need to talk about both my country's current water crisis + modern methods of agriculture and precision agriculture + overview of already existing materials and get to the research gap at the end)

## Slide 4
System Overview
CONTROLLER
SENSORS
WEATHER FORECAST
System
States
López-Jiménez et. al., 2024
“Agent-based model predictive control of soil-crop irrigation with topographical information,”
Control Engineering Practice, vol. 150, p. 106012, 2024.
4
Notes: Rain, ETc, Radiation, h2, h7, g
general objective (explaining necessary info of model and framing work as stress avoidance control under constraint)

## Slide 5
System Modeling and Dynamics
Growth function:
Drought stress:
Waterlogging stress:
Root zone
Field capacity
drought sensitivity
Thermal accumulation:
Heat stress:
Low temperature stress:
Base temperature
heat stress onset
Extreme heat
maturity threshold
maximum interception
GDD at 50% interception
5
Notes: system model (full description of my agent-based math model with special attention to key info)

## Slide 6
System Modeling and Dynamics
Water uptake coeff.
Wilting point
saturation
SCS curve-number threshold
Daily drainage coeff.
Heat stress maturation rate
Drought stress maturation rate
Radiation use efficiency
percipitation
irrigation
number of lower elevation neighbors
Infiltration:
Total surface water available:
Crop transpiration:
Surface runoff:
Deep vertical percolation:
6

## Slide 7
Control Problem Overview
Saturation
Field Capacity
Stress Threshold
Wilting Point
Waterlog Stress
Drought Stress
Desired Zone
Model Predictive Controller
Fixed-Schedule Controller
Reactive Controller
Soft Actor-Critic Controller (SAC)
Twin Delayed Deep Deterministic Policy Gradient (TD3)
7

## Slide 8
Heuristic Controllers
Reactive Controller
Fixed-Schedule Controller
8

## Slide 9
MPC Problem Statement
OBJECTIVE:
At each timestep k, find the control sequence that minimizes the cost function:
CONSTRAINTS:
9

## Slide 10
MPC Parameter Selection
10
Hp | Yield (kg/ha) | Mean solve time | Total wallclock/season
3 | 3791 | 3.2s | 0.05-0.1h
8 | 3810 | 23.5s | 0.7-1.4h
14 | 3819 | 105.0s | 1.0-7.6h
(price tier) | Yield (kg/ha) | Water (mm) | Waterlog-days
0.0004 (subsidized) | 3836 | 482 | 76.0
0.016 (domestic base) | 4142 | 468 | 1.8
0.044 (domestic tier D) | 4131 | 466 | 20.7
0.265 (industrial) | 1495 | 6 | 0.0
 | Yield (kg/ha) | Water (mm) | Waterlog-days
0.0004 (subsidized) | 3836 | 482 | 76.0
0.016 (domestic base) | 4142 | 468 | 1.8
0.044 (domestic tier D) | 4131 | 466 | 20.7
0.265 (industrial) | 1495 | 6 | 0.0
Selection of cost function parameters
Selection of Receding Horizon Hp
was chose as anchor. and had negligible variations through the sweep. and were chosen based on better performance on:
yield
total water amount used and
number of waterlog days.

## Slide 11
RL Controller Problem Statement
SAC:
11
OBJECTIVE:
Given the current state , find a policy that maximized the expected discounted return:
where
TD3:
(deterministic)
here includes a terminal bonus
(paid once at k=K)

## Slide 12
RL Controller Network Architecture
12
Linear
256 dims
LayerNorm
ReLU
Linear
Linear
67 dims
256 dims
Q
2
66 dims
128 dims
128 dims
128 dims
128 dims
SAC
TD3
CRITIC
ACTOR
LayerNorm
ReLU
LayerNorm
ReLU

## Slide 13: Primary Results
13
Controller | Yield (kg/ha) | % of Ceiling | Drought-days | Waterlog-days | Water Usage (mm) | Decision latency (ms)
No irrigation | 1728 | 43.5 | 86.5 | 1.4 | 0 | -
Fixed schedule | 3314 | 82.7 | 28.2 | 54.3 | 411 | -
Reactive controller | 3532 | 88.2 | 33.0 | 41.7 | 411 | -
SAC (Pool A) | 3785 | 94.6 | 25.6 | 18.2 | 382 | 1.0
SAC (Pool B) | 3777 | 94.4 | 32.4 | 16.1 | 376 | 1.0
MPC (Hp = 8) | 3810 | 95.2 | 16.0 | 7.7 | 364 | 52,603
TD3 (Pool B, 3-seed) | 3800 | 95.0 | 35.2 | 6.5 | 358 | 1.3
TD3 (Pool A, 3-seed) | 3805 | 95.1 | 33.7 | 7.2 | 362 | 1.3

## Slide 14: Mean ∆u Smoothing
15
Metric | MPC (Hp = 8) | TD3, , Pool A | TD3, , Pool B
Yield (kg/ha) | 3810 | 3811 | 3810
% of Ceiling | 95.2 | 95.2 | 95.2
Control effort, mean(mm/day) | 0.97 | 0.72 | 0.72
Drought-days | 16.0 | 33.2 | 35.3
Waterlog-days | 7.7 | 7.5 | 6.2
Water used (mm) | 364 | 363 | 359
Decision latency | ~53s | ~1.3ms | ~1.3ms
Metric | MPC (Hp = 8) |  | 
Yield (kg/ha) | 3810 | 3811 | 3810
% of Ceiling | 95.2 | 95.2 | 95.2
 | 0.97 | 0.72 | 0.72
Drought-days | 16.0 | 33.2 | 35.3
Waterlog-days | 7.7 | 7.5 | 6.2
Water used (mm) | 364 | 363 | 359
Decision latency | ~53s | ~1.3ms | ~1.3ms

## Slide 15: Per Scenario Analysis
14

## Slide 16: Robustness to Noise
Controller | %Yield, perfect | %Yield, noisy | ∆, pts
MPC (Hp = 8) | 95.2 | 95.0 | -0.23 pts
SAC (Pool A) | 94.6 | 93.8 | -0.78 pts
MPC (Hp = B) | 94.4 | 93.6 | -0.83 pts
TD3 (Pool A) | 95.1 | 94.9 | -0.21 pts
TD3 (Pool B) | 95.0 | 94.9 | -0.10 pts
TD3

## Slide 17: Conclusion
17
A model-free TD3 policy matches MPC's yield (99.7%, 3800 vs 3810 kg/ha) at ~1ms vs ~53s per decision and exceeds it on waterlog control and water efficiency.
Post-hoc EMA smoothing (α=0.3) closes 70% of TD3's control-effort gap to MPC.
A pool-composition decomposition shows ~70% of the apparent SAC-vs-TD3 drought gap was training-data artifact, not algorithm choice.

## Slide 18: THANK YOU FOR YOUR TIME!
taratorbati@yahoo.com
18